MIS 3200 Networking Fundamentals

Internet Questions

Student Name: ___________________________________________

| Your Home PC does not need a host name to get access to Internet services. | T | F |
| --- | --- | --- |
| Wide Area Information System refers to a service for searching index databases on remote computers. | T | F |
| Technically speaking, a DSL modem is not a modem. | T | F |

4.  Which of the following is not needed on the customer’s end in order to establish a DSL connection? (Choose all that apply)

- A switch

- Filter(s)

- UTP

- DSL modem

- DSLAM

5.  With Asymmetric DSL service, a standard telephone line is used to send/receive messages a high speed. This is possible because …

- The channel for voice transmission is used to transmit/receive message

- Other channels with smaller bandwidths are used to send/receive messages through the standard telephone line.

- Other channels with larger bandwidths are used to send/receive messages through the standard telephone line.

6.  Which of the following IP addresses ARE valid?

- 207.240.1.1

- 129.23.257.18

- 235.45.1.1

- 129.191.263.23

7. Using the conversion system illustrated below, convert the following IP address to dotted decimal notation: 10001011  01000101  00001000  00000011. (Spaces are included to facilitate reading.)

| If you know a web server’s IP address, you do not need to know its host name in order to access the web site it hosts using your web browser. | T | F |
| --- | --- | --- |

9.       DNS is a system that provides...

- Internet client computers with a temporary IP address when they requested one to use as their address for communications with other Internet hosts.

- Servers’ IP addresses given the servers’ host names.

- All of the above.

# Text boxes

Your answer:

10001011  =  ______

01000101  =  ______

00001000  =  ______

00000011  =  ______