MIS 3200 Networking Fundamentals

Internetworking Exercise 2

Consider the local area network shown in Figure 1 below.

Figure 1

Suppose that the bridging tables are as follow:

Assuming that the switch has been in operation for while, what computers and internetworking devices will receive the message if the following stations transmit?

1) Workstation 1 sends a message to workstation 2

_______________________________________________________________________

2) Workstation 2 sends a message to workstation 3

_______________________________________________________________________

3) Server 1 sends a message to workstation 3

_______________________________________________________________________

4) Workstation 3 sends a message to workstation 1

_______________________________________________________________________

# Text boxes

Port A table

Port B table

00-03-1F-F1-EB-59

01-04-1F-F1-BB-88

04-01-1G-00-YB-90

05-06-2F-U1-RR-55