## Slide 1: Failure Mode and Effect Analysis
(FMEA)
By Deyla Gonzalez & Jeffrey Heck

## Slide 2: FMEA – What Is It?
FMEA is an analytical method of identifying and prioritizing failure possibilities of a product, planning the correct action to prevent them, and documenting the complete process.
Notes: <number>

## Slide 3: FMEA – What Is A Failure Possibility?
Failure causes are any errors or defects in process, design, or item, especially those that affect the customer, and can be potential or actual.

## Slide 4: Why is FMEA Important?
Failure Mode and Effect Analysis allows a product development group to correct major defects BEFORE a product reaches the market.
THIS IS THE KEY TO A RELIABLE PRODUCT!

## Slide 5: First, Some FMEA Definitions
What is:
FMEA team components
Types of FMEA
Design FMEA
Process FMEA
Reliability

## Slide 6: FMEA – The Team
The FMEA team typically consists of representation from the following areas:
  Management Area
  Design Department
  Manufacturing Department
  Assembly Department
  Quality Control Department
  Service and Supply Departments
  End User

## Slide 7: Team Leader
The team leader, selected by the team, has the following responsibilities:
Determining the time and place of meetings.
Maintaining team communications.
Coordinating corrective action assignments and follow-ups.
Keeping files and records of FMEA forms.
Helping team members with form completion.
Maintaining constant progress in the FMEA processes.
Motivates team members to ensure their involvement.

## Slide 8: Types of FMEA
Design FMEA
Process FMEA

## Slide 9: Design FMEA
Design FMEA:
  Indentifies known and predictable failures.
  Ranks failures by relative impact on the product.
  Uncovers oversights and errors.
  Reduces development time and cost.
  Documents the results of the design FMEA process.

## Slide 10: Process FMEA
Process FMEA:
  Used to eliminate failures by indicating specific tests for the product.
  Determines which process variables need to be focused on for failure detection.
  Ranks failures by relative impact on the internal or external customer.
  Documents the results of the Process FMEA procedure.

## Slide 11: Reliability
Reliability is the ability of a system or component to perform its required functions under stated conditions for a specified period of time.

## Slide 12: Benefits of Design and Process FMEA
Captures the collective knowledge of a team.
Improves the quality, reliability, and safety of the process.
Creates a logical, structured process for identifying process areas of concern.
Reduces process development time and cost.

## Slide 13: Benefits of Design and Process FMEA (Continued)
Documents and tracks risk reduction activities.
Helps to identify characteristics that are critical to quality.
Provides historical records and establishes a baseline.
Helps increase customer satisfaction and safety.

## Slide 14: Starting the FMEA Process
A block diagram of the product/process needs to be developed to show the logical relationships between the components of the product or the steps/stages of the process. A block diagram may be in the form of boxes connected by lines, with each box corresponding to a major component of the product or a major step of the process. The lines correspond to how the product components or process steps are related to each other.
The Block Diagram

## Slide 15: Starting the FMEA Process
Start by making a list of all the components of the system.
Step 1 - The Block Diagram
The Radio Flyer
Part (Qty)
Wagon Bed (1)
Wheel (4)
Steering Hub (1)
Steering Yoke (1)
Rear Axle Assembly (1)
Rear Axle Brace (2)
Handle (1)
Friction Plate (2)
Safety Ball (1)

## Slide 16: Starting the FMEA Process
Then make a list of all the connection methods of the system.
Step 2 - The Block Diagram
The Radio Flyer
Connection Method
Cotter Pin and Nut
Locking Hubcap
Screw
Lock Nut

## Slide 17: Starting the FMEA Process
Lastly, construct the diagram by drawing a block representing each component connected by a line representing each connection method.
Step 3 - The Block Diagram

## Slide 18: The Design FMEA Document
FMEA Number: used for document tracking purposes.

## Slide 19: The Design FMEA Document
Item: used to clarify exactly which component is being analyzed.

## Slide 20: The Design FMEA Document
Design Responsibility: Identifies the Team responsible for this design. The name and department of the person or group responsible for preparing the document should also be included.

## Slide 21: The Design FMEA Document
Model Number / Year: Identifies the name and ID number of the system, subsystem, or component.

## Slide 22: The Design FMEA Document
Key Date: Contains the date that the initial FMEA is due.

## Slide 23: The Design FMEA Document
FMEA Date: Contains the original FMEA compilation date and the latest revision date.

## Slide 24: The Design FMEA Document
Core Team: Contains the names of the responsible individuals that have authority to perform tasks pertaining to this Design FMEA.

## Slide 25: The Design FMEA Document
Item / Function: Contains the name and ID number of the item being analyzed as well as one specific function of the item. Multiple functions should be listed and analyzed separately.

## Slide 26: The Design FMEA Document
Potential Failure Mode: Contains the method that:
May fail to meet design criteria.
May cause potential failure in a higher-level system.
May be the result of failure of a lower-level system.

## Slide 27: The Design FMEA Document
Potential Effect(s) of Failure (as perceived by the customer): Contains the method that:
May fail to meet design criteria.
May cause potential failure in a higher-level system.
May be the result of failure of a lower-level system.

## Slide 28: The Design FMEA Document
Severity: The assessment of the seriousness of the effect of the potential failure mode to the next sub-system, system, or customer if it occurs. (1 = No Effect, 10 = Failure affects safe operation and/or regulation noncompliance.)
Severity of Effect | Ranking
Hazardous Without Warning | 10
Hazardous With Warning | 9
Very High | 8
High | 7
Moderate | 6
Low | 5
Very Low | 4
Minor | 3
Very Minor | 2
None | 1

## Slide 29: The Design FMEA Document
Classification: Used to classify any special product characteristics for components, subsystems, or systems that may require additional process controls.

## Slide 30: The Design FMEA Document
Potential Cause(s) /Mechanism(s) Of Failure: All potential failure cause or mechanism must be listed completely and concisely. Examples: poor design, wrong materials, over-stressing, or inadequate life assumption, or poor lubrication.

## Slide 31: The Design FMEA Document
Occurrence: The chance that the specific causes/mechanisms will occur.
Probability of Failure | Possibility Failure Rates | Ranking
Very High: Failure Inevitable | >1 in 2 | 10
 | 1 in 3 | 9
High: Repeated Failures | 1 in 8 | 8
 | 1 in 20 | 7
Moderate: Occasional Failures | 1 in 80 | 6
 | 1 in 4000 | 5
 | 1 in 2000 | 4
Low: Relatively Few Failures | 1 in 15,000 | 3
 | 1 in 150,000 | 2
Remote: Failure Unlikely | 1 in 1,500,000 | 1

## Slide 32: The Design FMEA Document
Current Design Control: Activities that assure design sufficiency for the failure are listed here. Examples: prevention measures, design validation, and design verification.
Design controls are supported by:
Physical testing. 2. Mathematical studies.
Feasibility reviews. 4. Prototype testing
There are three types of design control that:
Prevent the cause/mechanism or failure mode effect from occurring or reduce the rate of occurrence.
Detect the cause/mechanism and lead to corrective actions.
Detect only the failure mode.

## Slide 33: The Design FMEA Document
Detection: This area is a relative measure of the assessment of the ability of the design control to detect either a potential cause/mechanism or the subsequent failure mode before the component, sub-system, or system is completed for production.
Detection | Ranking
Absolute Uncertainty | 10
Very Remote | 9
Remote | 8
Very Low | 7
Low | 6
Moderate | 5
Moderately High | 4
High | 3
Very High | 2
Almost Certain | 1

## Slide 34: The Design FMEA Document
Risk Priority Number: The product of the Severity, the Occurrence and the Detection rankings. Values can range from 1 to 1000 with 1 being the smallest design risk possible. This value allows the team to rank the issues on the form.
RPN = (S) X (O) X (D)

## Slide 35: The Design FMEA Document
Recommended Actions: Corrective actions examined by the Team. It is important to enter “None” if there are no recommended actions so that future teams will know that this was not overlooked.

## Slide 36: The Design FMEA Document
Responsibility and Target Completion Dates: This column lists the individual or group responsible for the recommended actions and the target completion date.

## Slide 37: The Design FMEA Document
Actions Taken: After an action has been taken the actual action and effective date should be entered in this column.

## Slide 38: The Design FMEA Document
Resulting RPN: After the corrective action has been identified, the severity, occurrence, and detection rankings should be re-estimated. Then the resulting RPN should be recalculated and recorded.

## Slide 39: The Process FMEA Document
Identifies all process functions and requirements.
Identifies all process and product failure modes.
Identifies process variable that requires focus for problem elimination.
Allows Team to determine the priority order of potential failure modes.
Produces documentation of the manufacturing/assembly process.

## Slide 40: The Process FMEA Document
Process Function Requirements: Contains the description of the process being analyized.

## Slide 41: The Process FMEA Document
Potential Failure Mode: Contains one of three types of failures:
How the process could fail to meet the process requirements.
The potential failure in a subsequent operation.
The effect associated with a previous operation.
Examples of Failure Modes include: | 
Cracked part | Friction with adjoining part
Poor support or bracing | Finish peeling or inadequate
Likely to loosen | Insufficient lubrication

## Slide 42: The ProcessFMEA Document
Potential Effect(s) of Failure (as perceived by the customer): The effects of the failure must be described from the customer viewpoint. Included, if present, is a statement as to the impact on personal safety or any violation of regulations.
Examples of Typical Failure Effects: | 
Customer Dissatisfaction | Safe Operation Impacted
Unacceptable Vibration | Unappealing Appearance
Intermittent Operation | Excessive Noise

## Slide 43: The Process FMEA Document
Severity: The assessment of the seriousness of the effect of the potential failure mode to the next sub-system, system, or customer if it occurs. (1 = No Effect, 10 = Failure affects safe operation and/or regulation noncompliance.)
Severity of Effect | Ranking
Hazardous Without Warning | 10
Hazardous With Warning | 9
Very High | 8
High | 7
Moderate | 6
Low | 5
Very Low | 4
Minor | 3
Very Minor | 2
None | 1
Notes: Same as Design FMEA
<number>

## Slide 44: The Process FMEA Document
Classification: Same as the Design FMEA. Used to classify any special product characteristics for components, subsystems, or systems that may require additional process controls.
Notes: Same as Design FMEA
<number>

## Slide 45: The Process FMEA Document
Potential Cause(s) /Mechanism(s) Of Failure: All potential failure causes or mechanisms must be listed completely and concisely. Only specific errors and malfunctions should be listed; ambiguous phrases should not be used.
Examples of Potential Causes of Failure: | 
Over-Tightening / Under-Tightening | Worn Quality Measuring Device
Tool Setup Error | Inadequate Training
Incorrect Fastening Materials | Inferior Third-Party Part Quality

## Slide 46: The Process FMEA Document
Occurrence: This is the same as the Design FMEA. The chance that the specific causes/mechanisms will occur.
Probability of Failure | Possibility Failure Rates | Ranking
Very High: Failure Inevitable | >1 in 2 | 10
 | 1 in 3 | 9
High: Repeated Failures | 1 in 8 | 8
 | 1 in 20 | 7
Moderate: Occasional Failures | 1 in 80 | 6
 | 1 in 4000 | 5
 | 1 in 2000 | 4
Low: Relatively Few Failures | 1 in 15,000 | 3
 | 1 in 150,000 | 2
Remote: Failure Unlikely | 1 in 1,500,000 | 1

## Slide 47: The Process FMEA Document
Current Process Control: This is the same as the Design FMEA. Activities that assure design sufficiency for the failure are listed here. Examples: prevention measures, design validation, and design verification.

## Slide 48: The Process FMEA Document
Detection: This area is an assessment of the probability that the proposed current process control will detect a potential weakness or failure before the part leaves the assembly location.
Detection | Ranking
Absolutely Impossible | 10
Very Remote | 9
Remote | 8
Very Low | 7
Low | 6
Moderate | 5
Moderately High | 4
High | 3
Very High | 2
Almost Certain | 1

## Slide 49: The Process FMEA Document
Detection: These area descriptions are much like the matching Design FMEA.

## Slide 50: Class Activity
Perform process FMEA to anticipate what you could do to eliminate any problems while changing a tire. Assume that you have just pulled off to the side of the road and have opened the trunk to remove the jack. Think of the process of replacing the tire and what you can put in place to avoid problems the next time you change a tire. Complete the process FMEA form.

## Slide 51: 10 Steps to Conduct a PFMEA
Step 1
Review the process—Use a process flowchart to identify each process component.
Step 2
Brainstorm potential failure modes—Review existing documentation and data for clues.
Step 3
List potential effects of failure—There may be more than one for each failure.
Step 4
Assign Severity rankings—Based on the severity of the consequences of failure.
Step 5
Assign Occurrence rankings—Based on how frequently the cause of the failure is likely to occur.

## Slide 52: 10 Steps to Conduct a PFMEA
Step 6
Assign Detection rankings—Based on the chances the failure will be detected prior to the customer finding it.
Step 7
Calculate the RPN—Severity X Occurrence X Detection.
Step 8
Develop the action plan—Define who will do what by when.
Step 9
Take action—Implement the improvements identified by your PFMEA team.
Step 10
Calculate the resulting RPN—Re-evaluate each of the potential failures once improvements have been made and determine the impact of the improvements.

## Slide 53
This presentation is concluded.
Thank for your attention!
Presenters / Authors:
Deyla Gonzalez
Jeffrey Heck